## Slide 1
Over-assist mitigation in column EPS: assist map versus PID torque feedback
Progress report: method, model, results, code
Tran Minh Tan | Supervisor: Dr. Phung Thanh Huy | HCMUT | 2026-10-10
Notes: Purpose: show the supervisor the method, model, results and code for the planned paper (Map vs PID).

## Slide 2
Main message
Closed-loop torque feedback removes the over-assist that the map cannot; both are limited by sensor noise times high-frequency gain
-14.1 %
Map: steady over-assist after mu 0.8 -> 0.3 while cornering (SLIP)
-0.09 %
PID: same situation, error returns to about zero
32 x
high-frequency gain of the map (lead) relative to PID: why the map is the noisiest
Same plant, sensors, actuator, cases and gates for every controller, fixed before tuning
PID tracks best on the calibration case (R 24.4 % vs map 32.2 %); PI is the smoothest
Open issue: no controller passes all four gates; gate values and the calibration case need a final decision

## Slide 3
Problem: over-assist when grip drops
The map is calibrated on a dry road and does not know mu
Assist map: T_a = M(v, |T_s|), calibrated so that T_s = T_d,ref at mu = 0.8
When mu drops while cornering, the self-aligning torque T_r of the front tires collapses
Same assist + smaller T_r = lighter steering than intended, exactly near the grip limit
Feedback alternative: track T_d,ref(v, a_y) with T_a; it needs a_y and a reference, but no estimate of mu
SLIP, last scene: mu 0.8 -> 0.3 at 48 s (0.35 g, 100 km/h)

## Slide 4
Model: closed loop shared by every controller
Plant - Sensors - controller - AssistLimit - Actuator, all at 1 ms; scoring on the true signals

## Slide 5
Model: plant and environment
Four states (theta2, theta2_dot, beta, gamma), driver = steering-angle source
Column: T_s = K (theta1 - theta2); J_col theta2_ddot = T_a - T_r + T_s - T_f tanh(c theta2_dot) - C_col theta2_dot
Tires: Pacejka Magic Formula, D = mu F_zf; T_r = (pneumatic trail + caster) F_yf / n_st
Vehicle: 2-DOF bicycle (beta, gamma) at constant speed; a_y = (F_yf + F_yr)/m
T_d,ref(v, a_y): 17 x 17 table; T_a,max(v) = demand + F (F = T_f = 2 N.m)
Sensors: noise (1 resolution step), quantization, 1 ms (T_s) / 10 ms (v, a_y via CAN)
Motor: clamp to +-T_a,max and first-order lag 100 Hz
parameter | value
K | 143.24 N.m/rad
J_col / C_col | 0.11 / 1.35
T_f | 2.0 N.m
m / Iz | 1573 kg / 2873 kg.m2
C_alpha_f | 160000 N/rad
column resonance | 6.1 Hz

## Slide 6
Method: one calibration case, three scoring cases
Tune on CALIB (local seed), score on DRY, SLIP, WEAVE (shared seed 99999)
CALIB 117 s
Dry; 20, 60, 100 km/h; 0.1-0.4 g, sine, small corrections; mu step 0.8 -> 0.6. Tuning only.
DRY 129 s
Steady torque on the dry road (map design condition). Main metric: max |e_rel|.
SLIP 63 s
Grip changes while cornering: puddle, mu rise, mu drop. Main metric: signed error after the change.
WEAVE 61 s
Continuous steering: slalom, lane change on mu 0.3, sine on mu 0.2. Main metric: RMS e_T, S, TV.

## Slide 7
Method: metrics, gates and selection rule
Written before tuning; one function per metric, shared by all controllers
metric | definition
R [%] | RMS e_T / mean ¦T_d,ref¦ in four window groups, equal weights
S [N.m] | RMS of T_a after a 5 Hz high-pass (assist-torque noise)
TV [N.m/s] | total variation of T_a per second
e_rel [%] | mean e_T / mean ¦T_d,ref¦ per steady window; < 0 = over-assist
gate (priority order) | threshold
1 stability with margin | gain x2 and +1 ms keep R < 2x
2 reverse assist | <= 1 % of time
3 no bang-bang | <= 1 % extra time at T_a,max
4 steady accuracy | ¦e_rel¦ <= 3 % in all windows
Selection: R within 5 % of the controller's own best R, then smallest S
Conclusion = compare whole Pareto fronts (R, S), not single points
Fallback if nothing passes: drop the lowest gate, take the least violation

## Slide 8
Controllers: assist map and PID
Map reads T_s and v only; PI/PID read T_s, v, a_y and the actuator clamp
Map (industrial baseline)
T_a = sgn(T_s) M(v, |T_s|) + lead (s/z+1)/(s/p+1) Dead zone 0.3 N.m, slope <= K_max K_acc = 6.75 (accuracy), K_stab = 9.5 (PM 45 deg), bang-bang K <= 7.5 Selected: K_max 6.75, z 59.8, p 1666 rad/s 1 tuned parameter, 11 simulations
PI / PID (torque feedback)
e_T = T_s - T_d,ref(v, a_y) T_a = Kp e_T + Ki int e_T + Kd d/dt T_s,meas / (Tf s + 1) Anti-windup on the clamp (Kaw = Ki/Kp) PI: Kp 1.25, Ki 3.0 (103 simulations) PID: Kp 1.50, Ki 3.0, Kd 0.015, Tf 3.5 ms (455 simulations)
 | Map | PI | PID
tuned parameters | 1 | 2 | 4
simulations on CALIB | 11 | 103 | 455
high-frequency gain | 188 | 1.25 | 5.8
signals read | T_s, v | T_s, v, a_y | T_s, v, a_y

## Slide 9
Result: column resonance and loop shape
The 6.1 Hz resonance caps the PI bandwidth; the map needs a large lead
Phase margin, discrete 1 ms model: Map 41, PI 12, PID 34 deg (Ms 1.8, 5.1, 1.9)
High-frequency gain: Map 188, PID 5.8, PI 1.25
Noise in T_a scales with this gain, not with the presence of a D term

## Slide 10
Result: tracking vs smoothness on CALIB
Whole Pareto fronts; stars are the selected points
 | R % | S N.m | TV
Map | 32.2 | 0.477 | 368
PI | 26.7 | 0.240 | 14
PID | 24.4 | 0.248 | 30
The map front lies to the right of the PI/PID fronts wherever S overlaps: the ranking does not depend on the choice of a single point.

## Slide 11
Result: steady accuracy on CALIB
Map meets the 3 % gate in 9 of 11 windows (fails at 0.4 g); PI/PID miss it only slightly at 0.1 g

## Slide 12
Result: scoring cases (noisy sensors, seed 99999)
Whole-case RMS tracking error and total variation of the assist torque
Chart: RMS e_T over the case [N.m]
| DRY | SLIP | WEAVE
Map | 0.644 | 0.6 | 1.308
PI | 0.485 | 0.381 | 0.709
PID | 0.453 | 0.35 | 0.643
TV of T_a [N.m/s] | Map | PI | PID
DRY | 325 | 19 | 36
SLIP | 330 | 24 | 41
WEAVE | 179 | 35 | 53
DRY max ¦e_rel¦ % | 2.75 | 1.58 | 1.90

## Slide 13
Result: over-assist in the SLIP case
Mean error in % of T_d,ref (negative = steering too light)
Window | meaning | Map | PI | PID
pud_in | inside 0.4 s puddle (mu 0.2), 80 km/h | -83.5 | -56.4 | -50.3
up_post | after mu 0.3 -> 0.8, 60 km/h, 0.15 g | 0.6 | -0.1 | -0.1
down_pre | before mu drop, 100 km/h, 0.35 g | 17.4 | -1.2 | -1.1
down_post | after mu 0.8 -> 0.3, settled | -14.1 | -0.1 | -0.1
After the friction drop the map settles at a lighter steering; PI and PID return to the reference (integral action and a_y-based reference)
Inside the 0.4 s puddle nobody can react fully, but the map error is the largest
This gap is structural (feedback + reference vs open-loop map), and is reported as such

## Slide 14
Open issues before freezing the method
Found while running all controllers under the same rules
Gates
No controller passes all four gates (reverse assist 1-4 %, e_rel > 3 %): points chosen by the fallback rule. The simulated margin gate accepted a PI with PM 12 deg (Ms 5.1): too weak. Thresholds need a source or a sensitivity study.
Calibration case
The mu step 0.8 -> 0.6 hardly changes T_r, so tuning does not see over-assist; only the scoring case SLIP does. Deeper step (e.g. 0.35) planned.
Model limits
Simulation only; open-loop driver (no recovery after a slide); motor as first-order lag; noise level assumed; plant not validated against vehicle data.
Gate (order) | Map | PI | PID
1 stable + margin (gain x2, +1 ms) | pass | pass | pass
2 reverse assist <= 1 % | fail (1.09) | fail (4.51) | fail (3.74)
3 no bang-bang (<= 1 % extra saturation) | pass | pass | pass
4 ¦e_rel¦ <= 3 % in all windows | fail (57.1) | fail (3.25) | fail (3.13)
linear PM / Ms (1 ms discrete model) | 41 deg / 1.8 | 12 deg / 5.1 | 34 deg / 1.9

## Slide 15
Code: MATLAB/Simulink R2023a, generated models
Every model is built by a script and has one test; all code and comments in English
Model/setup_paths.m paths (single place)
Model/data/*.json single data source
Model/PRSM/<Plant|Ref|Sensors|
AssistLimit|Actuator>/ build_*.m, test_*.m
Model/Controllers/<Map|PI|PID>/
load_<ctrl>.m, <Ctrl>.mdl, Model_<Ctrl>.mdl,
script/ design, sweep, select, test
Model/Sim/script/ build_closed_loop, make_cases,
calib_run, run_cases, make_pair_comparisons
Result/ Design, Calib, Cases, Compare
tools/build_report_en.py this report and deck
Run: setup_paths; load_pid; build_closed_loop('PID'); run_cases('PID', 10000)
Compare: make_pair_comparisons({'Map','PID'}, 99999)
Tests: test_plant, test_map, test_pid, test_calib, test_gates (all pass)
Repository: github.com/TanTramM/Adaptive-EPS-using-Reinforcement-Learning

## Slide 16
Planned paper and next steps
Paper: assist map vs PI/PID torque feedback; contributions: fair evaluation framework, resonance and high-frequency gain analysis, quantified over-assist
Next: settle gate values and the calibration mu step, freeze the method; sensitivity (gates, noise, seed); robustness to +-20 % plant errors; choose the venue. SMC/ISMC stay in the thesis.